## Slide 1: Network Layer:Routing

## Slide 2: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets traverse from given initial source host to final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 3
11.2 INTRA- AND INTERDOMAIN ROUTING
Today, an internet can be so large that one routing protocol cannot handle the task of updating the routing tables of all routers.
For this reason, an internet is divided into autonomous systems.
An autonomous system (AS) is a group of networks and routers under the authority of a single administration.
Routing inside an autonomous system is called intra-domain routing.
Routing between autonomous systems is called inter-domain routing

## Slide 4
Popular routing protocols

## Slide 5: Routing algorithm classification
global or decentralized information?
global: all routers have complete topology, link cost info
“link state” algorithms
decentralized: iterative process of computation, exchange of info with neighbors
routers initially only know link costs to attached neighbors
“distance vector” algorithms
How fast do routes change?
dynamic: routes change more quickly
  periodic updates or in response to link cost changes
static: routes change slowly over time

## Slide 6: Graph abstraction: link costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
ca,b: cost of direct link connecting a and b
e.g., cw,z = 5, cu,z = ∞
  cost defined by network operator: could always be 1, or inversely related to bandwidth, or inversely related to congestion
N: set of routers = { u, v, w, x, y, z }
E: set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 7: Dijkstra’s link-state routing algorithm
centralized: network topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (“source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k destinations
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
N': set of nodes whose least-cost-path definitively known
notation

## Slide 8: Dijkstra’s link-state routing algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes v
4 if v adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(v) = cu,v /* but may not be minimum cost! */
6 else D(v) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' :
D(v) = min ( D(v), D(w) + cw,v )
/* new least-path-cost to v is either old least-cost-path to v or known
least-cost-path to w plus direct-cost from w to v */

## Slide 9: Dijkstra’s algorithm: an example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
4,x
3,y
3,y
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
Initialization (step 0): For all a: if a adjacent to then D(a) = cu,a

## Slide 10: Dijkstra’s algorithm: an example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
4,x
3,y
3,y
u
y
x
w
v
z
resulting least-cost-path tree from u:
resulting forwarding table in u:
v
x
y
w
x
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
outgoing link
route from u to v directly
route from u to all other destinations via x

## Slide 11: Dijkstra’s algorithm: another example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9

## Slide 12: Dijkstra’s algorithm: discussion
algorithm complexity: n nodes
each of n iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2) complexity
message complexity:
each router must broadcast its link state information to other n routers
each router’s message crosses O(n) links: overall message complexity: O(n2)

## Slide 13: Dijkstra’s algorithm: oscillations possible
when link costs depend on traffic volume, route oscillations possible
a
d
c
b
1
1+e
e
0
e
1
1
0
0
initially
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
a
d
c
b
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
sample scenario:
  routing to destination a, traffic entering at b, c, d with rates 1, e (<1), 1
  link costs are directional, and volume-dependent
e
1
1
e
1
1
e
1
1

## Slide 14: Distance vector algorithm
Based on Bellman-Ford (BF) equation:
Let Dx(y): cost of least-cost path from x to y.
Then:
Dx(y) = minv { cx,v + Dv(y) }
Bellman-Ford equation
min taken over all neighbors v of x
v’s estimated least-cost-path cost to y
direct cost of link from x to v

## Slide 15: Bellman-Ford Example
u
y
z
2
2
1
3
1
1
2
5
3
5
Suppose that u’s neighboring nodes, x,v,w, know that for destination z:
Du(z) = min { cu,v + Dv(z),
cu,x + Dx(z),
cu,w + Dw(z) }
Bellman-Ford equation says:
Dv(z) = 5
v
Dw(z) = 3
w
Dx(z) = 3
x
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum (x) is next hop on estimated least-cost path to destination (z)

## Slide 16: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
Dx(y) ← minv{cx,v + Dv(y)} for each node y ∊ N
when x receives new DV estimate from any neighbor, it updates its own DV using B-F equation:

## Slide 17: Distance vector algorithm:
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
wait for (change in local link cost or msg from neighbor)
each node:
distributed, self-stopping: each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors – only if necessary
  no notification received, no actions taken!
recompute DV estimates using DV received from neighbor
if DV to any destination has changed, notify neighbors

## Slide 18
x
z
1
2
7
y

## Slide 19
A graph for Bellman-Ford algorithm

## Slide 20
When to Share Routing Table
Periodic Update
  A node sends its routing table, normally 30 seconds, in a periodic update
Triggered Update
  A node sends its routing table to its neighbors any time when there is a change in its routing table
    1. After updating its routing table, or
    2. Detects some failure in the neighboring links

## Slide 21
In distance vector routing, each node shares its routing table with its immediate neighbors periodically and when there is a change.
Note:

## Slide 22
Figure Two-node instability

## Slide 23: Distance vector: link cost changes
link cost changes:
node detects local link cost change
“bad news travels slow” – count-to-infinity problem:
x
z
1
4
50
y
60
y sees direct link to x has new cost 60, but z has said it has a path at cost of 5. So y computes “my new cost to x will be 6, via z); notifies z of new cost of 6 to x.
z learns that path to x via y has new cost 6, so z computes “my new cost to x will be 7 via y), notifies y of new cost of 7 to x.
y learns that path to x via z has new cost 7, so y computes “my new cost to x will be 8 via y), notifies z of new cost of 8 to x.
z learns that path to x via y has new cost 8, so z computes “my new cost to x will be 9 via y), notifies y of new cost of 9 to x.
…
see text for solutions. Distributed algorithms are tricky!